Déjà Vu Byte Code Design Document and Documentation

# File Format
## Header
The header consists of the following parts:
1. The magic byte sequence 07 44 56 (BEL “D” “V”). This sequence was chosen to be unlikely be mistaken for plain text in most contexts, and to give an audible bell when possible, as well as identify this as Déjà Vu byte code. Additionally, this sequence together with the version byte takes exactly four bytes, which aligns everything on four byte boundaries.
2. A single byte describing the byte code version, the first four bits denoting the major revision, the last four bits denoting the minor revision. This version is 02.
3. Four bytes, read as an big endian unsigned integer, specifying code length, which is the total number of instructions.
4. The code, explained in the next section.
5. The literals, explained in the section after that.
## Main code
Each instruction consists of four bytes: a single byte for the instruction, and three additional bytes used as an argument to the opcode. The argument is always taken as a bigendian value. It can be:
- An unsigned integer value, for the index in the list of literals.
- A signed integer value, for the offset for a jump.
- A signed integer value, for short integer literal numbers in the source.
- Any value, for opcodes that do not take an argument. Generally, the byte code compiler will produce a value of zero for such opcodes, but it is not guaranteed.
## Literals
All literals contained in Déjà Vu source code are collected and listed at the end of the byte code. This way they can be referenced by a single number anywhere in the byte code file.
# Instruction Opcodes
## Opcode sections
Section	Offset
Words and literals	00000000
Flow control	00010000
Scope control	00100000
List control	00110000
Stack control	01000000
Debug information	01010000
Error handling	01100000
Dict control	01110000

## Opcodes
Opcode	Section	Value
PUSH_LITERAL	Words and literals	00000000
PUSH_INTEGER	Words and literals	00000001
PUSH_WORD	Words and literals	00000010
SET	Words and literals	00000011
SET_LOCAL	Words and literals	00000100
SET_GLOBAL	Words and literals	00000101
GET	Words and literals	00000110
GET_GLOBAL	Words and literals	00000111
JMP	Flow control	00010000
JMPZ	Flow control	00010001
RETURN	Flow control	00010010
RECURSE	Flow control	00010011
LABDA	Scope control	00100000
ENTER_SCOPE	Scope control	00100001
LEAVE_SCOPE	Scope control	00100010
NEW_LIST	List control	00110000
POP_FROM	List control	00110001
PUSH_TO	List control	00110010
PUSH_THROUGH	List control	00110011
DROP	Stack control	01000000
DUP	Stack control	01000001
SWAP	Stack control	01000010
ROT	Stack control	01000011
OVER	Stack control	01000100
LINE_NUMBER	Debug information	01010000
SOURCE_FILE	Debug information	01010010
ENTER_ERRHAND	Error handling	01100000
LEAVE_ERRHAND	Error handling	01100001
NEW_DICT	Dict control	01110000
HAS_DICT	Dict control	01110001
GET_DICT	Dict control	01110010
SET_DICT	Dict control	01110011

# Literal Data
Type	Value
Ident	00000000
String	00000001
Number	00000010

For idents and strings, the following four bytes (bigendian, unsigned int) designate length, the first n bytes after that are a UTF-8 encoded string. Idents starting with the hash character (#) are compiler-generated names for hidden variables, since the use of a hash character inside a literal ident is forbidden.
For numbers, the type is followed by eight bytes, which is read as a double precision floating point number.
# Modules
## Definition
A module is a Déjà Vu program, which is run the first time when the word use is called with its name on top of the stack.
## Locations
# Discussion
## Module system
Possible solutions:
- Keep current solution.
- Implement more advanced module system, appending file extensions.
# Changes
- This version adds a new datatype (dict), a new byte code section (Dict control) and four opcodes in that section (NEW_DICT, HAS_DICT, GET_DICT and SET_DICT).
- It defines three new opcodes in the List control section (POP_FROM, PUSH_TO and PUSH_THROUGH)
- It defines three new opcodes in the Stack control section (SWAP, ROT and OVER)